CHEROKEE NATION

REQUEST FOR SEALED PROPOSALS

CONSTRUCTION MANAGEMENT

AT-RISK SERVICES

PROJECT:  CENTRAL OFFICE BUILDING SPECIFICATIONS & DRAWINGS

The new Cherokee Nation Central Office Building is a state-of-the-art facility that will be located in Tahlequah, Oklahoma.

Program:

The Central Office Building project consists of approximately 70,000 building gross square feet (BGSF).   The main purpose of the project is to provide conference space and a data center for the Cherokee Nation.   The conference center is to have an associated catering kitchen that can also serve a grab and go café in the lobby of the building.  There are two upper floors, with four suites each, intended for miscellaneous government departments, which will be served by a grand stair as well as two public elevators, and two fire  stairs on either side of the building.  The primary occupancy of the building is anticipated to be B-Business.   Currently, there are two structures on the site to be demolished as part of the scope of the project.

Systems:

Mechanically, the basis of design is roof-top, light package units.  There will be units on the roof of Level 1, and others on the roof of Level 2.

Structurally, the basis of design is steel moment frame.  In order to provide maximum flexibility to the office  spaces on levels 2 and 3, there should be minimal to no braced frames as part of the project.  In response  to the local environment, there will be hardened areas within the building.  It is anticipated that the data center and associated work room will be hardened, as well as one other area of  approximately 4,500 SF.  These hardened areas are intended to be grout filled, reinforced CMU block, with  a concrete lid.

The data center will require a secondary cooling system with redundancy.  Two CRAC units to supply air via underfloor plenum in the recesses slab.  Floor tiles to be adjustable.

Please utilize the following hyperlinks for project specifications and drawings.

Hyperlinks:

01_Site Plan

02_Current Floor Plans

03_Renderings

Design Development